## Slide 1: The Memory
Hierarchy
14

## Slide 2: This is a Pyramid Scheme
But this knowledge is a safe investment.

## Slide 3: Wanting Moore and Moore
Processors and memory work together but improve at different rates.
Memory was initially faster than CPU, but its innovation was slower.
Throughput
1950
1960
1970
1980
1990
2000
2010
2020
1
10
100
1000
10000
0.1
0.01
The CPU overtakes memory performance
Innovation starts to slow

## Slide 4: Cost of DRAM/Disk in 2020
8GiB $35 - 70
16GiB $70 - 100
32GiB $140 - 300
1TiB $50 – 80
8TiB $200 - $300
16TiB $400 - 500
nanoseconds
milliseconds

## Slide 5: The memory hierarchy
Faster,
Denser
Expensive
Cheaper,
Slower,
Larger
Registers
L1 Cache
L2 Cache
(DRAM) Main Memory
Local Disk
Distributed Storage
(Don’t forget it!) Tape

## Slide 6: The hierarchy of speed
Faster,
Denser
Expensive
Cheaper,
Slower,
Larger
Registers
L1 Cache
L2 Cache
(DRAM) Main Memory
Local Disk
Distributed Storage
(Don’t forget it!) Tape
DRAM is simply too slow
A “cache” is used to hold useful data closer than main memory to improve speed.

## Slide 7: Memory Hierarchy: Core 2 Duo
Disk
Main Memory
L2 unified cache
L1
I-cache
L1
D-cache
CPU
Reg
2 B/cycle
8 B/cycle
16 B/cycle
1 B/30 cycles
Throughput:
Latency:
100 cycles
14 cycles
3 cycles
millions
~4 MB
32 KB
~8 GB
~500 GB
Not drawn to scale
Miss Penalty
(latency)
33x
Miss Penalty
(latency)
10,000x
SRAM
Static Random Access Memory
DRAM
Dynamic Random Access Memory

## Slide 8: Memory Caching
Cache: Another thing us teachers could really use more of.

## Slide 9: Experiment: Scientific Maths
#include <stdlib.h> // for malloc
#define LIMIT (2048 * 10)
int main(void) {
int i, j;
int* src[LIMIT];
int* dst[LIMIT];
for (i = 0; i < LIMIT; i++) {
src[i] = malloc(sizeof(int) * LIMIT);
dst[i] = malloc(sizeof(int) * LIMIT);
}
for (j = 0; j < LIMIT; j++) {
for (i = 0; i < LIMIT; i++) {
dst[j][i] = src[j][i];
}
}
return 0;
}
#include <stdlib.h> // for malloc
#define LIMIT (2048 * 10)
int main(void) {
int i, j;
int* src[LIMIT];
int* dst[LIMIT];
for (i = 0; i < LIMIT; i++) {
src[i] = malloc(sizeof(int) * LIMIT);
dst[i] = malloc(sizeof(int) * LIMIT);
}
for (j = 0; j < LIMIT; j++) {
for (i = 0; i < LIMIT; i++) {
dst[i][j] = src[i][j];
}
}
return 0;
}
> time ./locality-test-A
real 0m1.803s
user 0m1.123s
sys 0m0.677s
> time ./locality-test-B
real 0m20.374s
user 0m19.429s
sys 0m0.898s

## Slide 10: Practical Performance
Caching is necessary for the utility of computers.
  The CPU/Memory gap increases (The Memory Wall)
In order to actually use these fast CPUs, we need to improve the apparent speed of RAM.
  Programs use memory a whole lot.
  The bottleneck would grind performance to the point where CPUs cannot improve.
“That’s a nice CPU you have there… it’d be terrible if something were to happen to it.”

## Slide 11: The problem: data is faaaaar away
?
Let’s say you want to read a book.
You check it out of the library.
  You have to go there.
  Find the book.
  Maybe take the bus back.
    Wait in traffic.
Now it sits on your desk.
  As long as it is near you, it’s easy to access the information.
  Yet, if you need another book…
    You would take the book ALL THE WAY back! (bare with me)

## Slide 12: Caching: Keeping things close
?
Let’s say you want to read a book.
  It’s not on your bookshelf.
So, still have to check it out of the library.
  You gotta go there. Find the book. Etc.
  Take the bus back.
Now it sits on your desk.
  As long as it is near you, it is easy to access the information.
  When we need another book… we put it aside.
    Maybe a bookshelf.
  The next time we need it, it will be nearby.

## Slide 13: The metaphorical cache
The bookshelf is a cache.
  It holds information that you might want later.
It is [much] smaller than a library, but faster to retrieve things.
However, it is small. Placing a new book on the shelf may require taking an old book off.

## Slide 14: Memory cache (CPU)
RAM is the library. It is far away and getting stuff from there is slow.
To better handle the performance gap between the CPU and memory we add a smaller, fast memory near the CPU.
This is the CPU cache.

## Slide 15: Data, the journey
?
When data is requested, the goal is to read a word into a CPU register.
The CPU first contacts the cache and asks if it has a copy.
  If it does… that is a cache hit, and, well, that was easy. Just copy that value into the register.
If it does not, this is a cache miss.
  It will then contact the next component in the memory hierarchy. (RAM)
Ram copies the value to cache, and the cache copies the value to the register.
%rax
mov (%rbx), %rax

## Slide 16: Missing the mark
8
8
When the CPU requests memory in an empty cache, the data obviously won’t be available locally.
This is a compulsory miss, a “miss” due to the first access of a block of data.
  Also known as a “cold miss.”
These are, as they suggest, completely unavoidable.
  They always incur the high penalty associated with a memory read.
?
0
%rax
1
2
3
4
5
6
7
8
9
A
B
C
D
E
mov (0x8), %rax
8
CPU Cache
RAM

## Slide 17: Hitting the target
8
8
8
When the CPU requests memory that happens to already be in the cache, the data is read locally (quickly).
This is a cache hit.
  Your best-case scenario.
These avoid having to communicate at all with memory.
  No penalty taken for reading/writing to memory.
  Very cheap in terms of time.
?
0
%rax
1
2
3
4
5
6
7
8
9
A
B
C
D
E
mov (0x8), %rax
CPU Cache
RAM

## Slide 18: A cache half full…
8
E
4
6
C
1
8
As the CPU requests memory, the cache will fill to satisfy each compulsory miss.
When it fills up completely, it will have no further room for the next miss.
On a miss, it requests the data from memory.
  Yet, where does it go?? We must remove one.
This is a capacity miss. The memory requirements of the program are larger than the cache.
?
0
%rax
1
2
3
4
5
6
7
8
9
A
B
C
D
E
mov (0x8), %rax
8
CPU Cache
RAM

## Slide 19: Looking closer…
8
4
6
C
1
8
It is difficult to know what block of data to omit from this cache on such a miss.
  However we can exploit the common locality patterns of programs to improve our cache.
There is temporal locality: accessed data is likely to be used again in near future.
  This is what caches generally capture.
However, spatial locality is also likely: data is often grouped together.
  When we access a struct field, we will often access another which is nearby in memory.
0
%rax
1
2
3
4
5
6
7
8
9
A
B
C
D
E
CPU Cache
RAM

## Slide 20: Exploring space…
8
We would like to keep data that is adjacent in memory in the cache, together, at the same time.
To do this, we “hash” the address. This is used to determine the cache slot.
  Just a fancy way to say: we divide the address by the cache size and use the remainder.
Every 0th block, 1st block, 2nd block, etc.
The 5th block (in this example) goes to the 0 slot, the 6th goes to the 1 slot, and so on.
0
%rax
1
2
3
4
5
6
7
8
9
A
B
C
D
E
CPU Cache
0
1
2
3
4
RAM

## Slide 21: Direct and to the point…
8
Let’s read addresses 3, 4, 5, 6, and 7 (in that order) from memory.
Reading address 8 next incurs a capacity miss, but it evicts the address that is furthest away from the others.
  This type of cache is good for programs that read through data sequentially.
  That is because such programs will always remove the least recently used block on a miss, as shown here.
Because every address has a specific cache slot, this is called a direct-mapped cache.
0
%rax
1
2
3
4
5
6
7
8
9
A
B
C
D
E
CPU Cache
0
1
2
3
4
RAM
3
3
4
4
5
6
7
5
6
7
8
8

## Slide 22: Missing your connection…
A
Let’s consider an antagonist pattern.
  What is the worst case for this cache?
If we read every 5th address in our memory in order, we would overwhelm our direct-mapped cache.
  Let’s access 0, 5, A in that order.
Accessing address 0 is a compulsory miss.
  Address 5, however, is a miss.
  But our cache isn’t full!!
A miss that occurs even though your cache could fit the block is called a conflict miss.
0
%rax
1
2
3
4
5
6
7
8
9
A
B
C
D
E
CPU Cache
0
1
2
3
4
RAM
0
5
A
0
5
A

## Slide 23: How big is that block?
Spatial locality is SO prevalent that it makes a whole lot of sense to pull more data than is requested.
  If we request a word (8 bytes) from memory, and we have a cache miss, let’s pull 8 words at a time (64 bytes).
Therefore, the blocks visualized to the right can have a size, called the block size.
  The bigger the block, the better spatial locality will become.
  However, the more time it takes to copy from memory and the higher penalty if you throw it away on a miss!
0
%rax
1
2
3
4
5
6
7
8
9
A
B
C
D
E
CPU Cache
0
1
2
3
4
RAM
64 bytes
8 bytes

## Slide 24: Block size helps locality
2
2
When we request an address from our cache, we are requesting the block that contains that address.
  Here, Block 0 contains byte addresses 0x00 through 0x39. Block 1 is 0x40 to 0x79, etc.
Let’s request 64-bit words in order starting at address 0x40 (Block 1)
  There are 8 words in each cache block.
  Therefore, we have only one compulsory miss.
  And then we have 7 cache hits!!
If we request the ninth word, we will be at address 0x80 (and a compulsory miss.)
0
%rax
1
2
3
4
5
6
7
8
9
A
B
C
D
E
CPU Cache
0
1
2
3
4
RAM
64 bytes
1
1

## Slide 25: Once again… A Tale of Two C… um… programs
#include <stdlib.h> // for malloc
#define LIMIT (2048 * 10)
int main(void) {
int i, j;
int* src[LIMIT];
int* dst[LIMIT];
for (i = 0; i < LIMIT; i++) {
src[i] = malloc(sizeof(int) * LIMIT);
dst[i] = malloc(sizeof(int) * LIMIT);
}
for (j = 0; j < LIMIT; j++) {
for (i = 0; i < LIMIT; i++) {
dst[j][i] = src[j][i];
}
}
return 0;
}
#include <stdlib.h> // for malloc
#define LIMIT (2048 * 10)
int main(void) {
int i, j;
int* src[LIMIT];
int* dst[LIMIT];
for (i = 0; i < LIMIT; i++) {
src[i] = malloc(sizeof(int) * LIMIT);
dst[i] = malloc(sizeof(int) * LIMIT);
}
for (j = 0; j < LIMIT; j++) {
for (i = 0; i < LIMIT; i++) {
dst[i][j] = src[i][j];
}
}
return 0;
}
> time ./locality-test-A
real 0m1.803s
user 0m1.123s
sys 0m0.677s
> time ./locality-test-B
real 0m20.374s
user 0m19.429s
sys 0m0.898s
Allocates matrices.
(Array of arrays)
Copies one matrix to another.
(data itself is uninitialized.)
Iterates through column.
(Other code goes through row)
SERIOUS

## Slide 26: Once again… A Tale of Two C… um… programs
We will simplify by looking at a 4x4 matrix.
  We want to get the addresses being used to see the access pattern. (Goes across row)
#include <stdlib.h> // for malloc
// We will look at a 4 by 4 matrix
int main(void) {
int i, j;
int* src[4];
int* dst[4];
for (i = 0; i < 4; i++) {
src[i] = malloc(sizeof(int) * 4);
dst[i] = malloc(sizeof(int) * 4);
}
for (j = 0; j < 4; j++) {
for (i = 0; i < 4; i++) {
dst[j][i] = src[j][i];
}
}
return 0;
}
src[0]
0x80
0x84
0x88
0x8c
src[1]
0x90
0x94
0x98
0x9c
src[2]
0xa0
0xa4
0xa8
0xac
src[3]
0xb0
0xb4
0xb8
0xbc
0x80
0x84
0x88
0x8c
0x90
0x94
0x98
0x9c
0xa0
src[0][0]
src[0][1]
src[0][2]
src[0][3]
src[1][0]
src[1][1]
src[1][2]
src[1][3]
src[2][0]
0xa4

## Slide 27: Once again… A Tale of Two C… um… programs
0x82
We will simplify by looking at a 4x4 matrix.
  Notice the different type of access pattern.
  (Goes down the column)
src[0]
0x80
0x84
0x88
0x8c
src[1]
0x90
0x94
0x98
0x9c
src[2]
0xa0
0xa4
0xa8
0xac
src[3]
0xb0
0xb4
0xb8
0xbc
0x80
0x90
src[0][0]
src[1][0]
#include <stdlib.h> // for malloc
// We will look at a 4 by 4 matrix
int main(void) {
int i, j;
int* src[4];
int* dst[4];
for (i = 0; i < 4; i++) {
src[i] = malloc(sizeof(int) * 4);
dst[i] = malloc(sizeof(int) * 4);
}
for (j = 0; j < 4; j++) {
for (i = 0; i < 4; i++) {
dst[i][j] = src[i][j];
}
}
return 0;
}
0xa0
0xb0
src[2][0]
src[3][0]
0x84
0x94
src[0][1]
src[1][1]
0xa4
0xb4
src[2][1]
src[3][1]

## Slide 28: The Antagonist
0x180
One program reads words sequentially in memory (good spatial locality)
  The other reads each word as far apart as possible! (worst spatial locality)
Let’s look at making the matrices much larger! Let’s make each row span 256 Bytes. (4 blocks, which is the size of our cache!)
0x80
0x84
0x88
0x8c
0x90
0x94
0x98
0x9c
0xa0
0xa4
0xa8
0xac
0x80
0x84
0x88
0x184
0x188
0x280
0x284
0x288
0x380
0x384
0x388
0
1
2
3
CPU Cache (256 Bytes)
0
1
2
3
RAM
Cache size: 256B
64 bytes per block.
Miss
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Miss
Miss
Miss
Miss
Miss
Miss
Miss
Miss
Miss
Miss
Miss
This cache item holds 0x000, 0x100, 0x200, etc

## Slide 29: Cache Performance
  Why? Well…
  Our “slow” program effectively did not use cache, and it was 10 times slower.
Simply: Caches offer much faster accesses than DRAM.
  Perhaps 100s of times faster.
Consider the math:
  miss rate (MR): Fraction of memory accesses not in cache.
  hit rate (HR): Fraction of memory accesses found in cache. ( )
  hit time (HT): Time it takes to read a block from cache to CPU. (Best case)
  miss penalty (MP): Time it takes to read from main memory to cache.
Recall that caches make computers practical.

## Slide 30: Cache Performance
Consider the math:
  miss rate (MR): Fraction of memory accesses not in cache.
  hit rate (HR): Fraction of memory accesses found in cache. ( )
  hit time (HT): Time it takes to read a block from cache to CPU. (Best case)
  miss penalty (MP): Time it takes to read from main memory to cache.
Average Memory Access Time (AMAT): The time it takes, on average, to perform a memory request, considering the cache performance.
Assuming a HT of 1 clock cycle and a MP of 100 clock cycles…
  A HR of 97%:
  A HR of 99%:
  A hit-rate jump from just 97% to 99% doubles memory performance. Wow.
Recall that caches make computers practical.

## Slide 31: Cache Layout Summary
We have seen two types of cache layouts.
  A freeform cache: blocks go wherever. ¯\_(ツ)_/¯
    Also called a fully associative cache.
  A direct-mapped cache: blocks go into slots.
They have their own trade-offs, and as usual…
  We can have a hybrid approach!
Here, each cache slot has multiple bins.
  You only need to evict when you fill up the bins. Best of both worlds!
  Which do you evict? (Hmm… difficult choice.)
CPU Cache
(direct-mapped)
0
1
2
3
4
CPU Cache
(fully associative)
CPU Cache
(2-way associative)
0
1
2
3
4

## Slide 32: Associativity
With an associative cache, the address determines the slot.
  Much like a direct-mapped cache.
  However, the slot has a number of bins.
  Any bin in the slot is viable for a block.
  The number of bins is the number of “ways”
    A direct-mapped cache is a 1-way cache.
When the cache determines if the block is in the cache already…
  It determines the slot.
  It scans every bin for a block tagged with that exact address.
  Therefore, the cache performance degrades as you increase the number of ways.
CPU Cache
(4-way associative)
0
1
2
CPU Cache
(2-way associative)
0
1
2
3
4
5

## Slide 33: Another way of viewing it
CPU Cache
(2-way associative)
0
1
2
3
CPU Cache
(fully associative)
0
CPU Cache
(direct-mapped)
(1-way associative)
0
1
2
3
4
5
6
7
All have the same size, so…
On a fully associative cache all blocks belong to the same set
On a direct-mapped cache all blocks belong to a different set
On a n-way associative cache n blocks belong to the same set

## Slide 34: Mapping
WT F…Cache!?

## Slide 35: Sooo… exactly what can go where?
Given a memory address, in which set does it go?
How many sets are there?
Let’s start by defining a cache size
  32KiB
How many cache lines do you need?
  Well it depends on the size of each cache line
    # Cache line? # Cache row? # Block? # bins?
  Let’s use: 64B!
64B
I need lines

## Slide 36: Sooo… exactly what can where?
Let’s start by defining a cache size
  32KiB
How many cache rows do you need?
  Well it depends on the size of each row
  Let’s use: 64B!
Decrease the size
  +rows, + (but faster) memory access, -locality
Increase the size
  -rows, -(but slower) memory access, +locality
64B
I need rows

## Slide 37: How many sets
The number of sets depends on the associativity
  Remember we have a fixed amount of rows!
For fully associative (easy) we have 1 set 
For n-way associative cache we need some maths:
  n-way associative means we divide the lines in groups of n-elements
Still rows!
Each column (set) has n rows
0
…
s-1
So how many sets?

## Slide 38: How many sets
If we apply this to a 4-way associative cache
Each column (set) has 4 rows
0
…
127
So how many sets?
Still rows!

## Slide 39: Address Manipulation
Request from CPU:
-bit virtual address
Page offset
Virtual Page Number
Access PT:
-bit physical address:
Page offset
Physical Page Number
Offset
Set Index
Cache Tag
Split to access cache:
TRANSLATION
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 40: Using our example
On our example:
  Cache size: 32KiB
  Block size: 64B =
  Associativity: 4-way
  Number of sets: 128 =
-bit physical address:
Page offset
Physical Page Number
Offset
Set Index
Cache Tag
Split to access cache:
6 bits
7 bits
12 bits
TAG | Set | valid | Data
0xFFF | 0 | 0 | (64B of data)
0xFFF | 0 | 1 | (64B of data)
0xFFF | 1 | 1 | (64B of data)
0x123 | 1 | 1 | (64B of data)
0x456 | 42 | 1 | (64B of data)
0xFFF | 42 | 1 | (64B of data)
Only showing 2 blocks per set (slide space)
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 41: Using our example
-bit physical address:
0000000
111111111111000000
0
0
0xFFF
Split to access cache:
6 bits
7 bits
12 bits
TAG | Set | valid | Data
0x000 | 0 | 0 | (64B of data)
0xFFF | 0 | 1 | (64B of data)
0xFFF | 1 | 1 | (64B of data)
0x123 | 1 | 1 | (64B of data)
0x456 | 42 | 1 | (64B of data)
0xFFF | 42 | 1 | (64B of data)
Hit!
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 42: Using our example
-bit physical address:
0000000
000000000000000000
0
0
0x000
Split to access cache:
6 bits
7 bits
12 bits
TAG | Set | valid | Data
0x000 | 0 | 0 | (64B of data)
0xFFF | 0 | 1 | (64B of data)
0xFFF | 1 | 1 | (64B of data)
0x123 | 1 | 1 | (64B of data)
0x456 | 42 | 1 | (64B of data)
0xFFF | 42 | 1 | (64B of data)
Miss!
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 43: Using our example
-bit physical address:
1000000
000100100011000000
0
1
0x123
Split to access cache:
6 bits
7 bits
12 bits
TAG | Set | valid | Data
0x000 | 0 | 0 | (64B of data)
0xFFF | 0 | 1 | (64B of data)
0xFFF | 1 | 1 | (64B of data)
0x123 | 1 | 1 | (64B of data)
0x456 | 42 | 1 | (64B of data)
0xFFF | 42 | 1 | (64B of data)
Hit!
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 44: Using our example
-bit physical address:
0000000
101010101010010101
0
42
0xAAA
Split to access cache:
6 bits
7 bits
12 bits
TAG | Set | valid | Data
0x000 | 0 | 0 | (64B of data)
0xFFF | 0 | 1 | (64B of data)
0xFFF | 1 | 1 | (64B of data)
0x123 | 1 | 1 | (64B of data)
0x456 | 42 | 1 | (64B of data)
0xFFF | 42 | 1 | (64B of data)
Miss!
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 45: Offset
-bit physical address:
0000010
111111111111000000
2
0
0xFFF
Split to access cache:
6 bits
7 bits
12 bits
63 | 62 | 61 | … | 5 | 4 | 3 | 2 | 1 | 0
0xF5 | 0x32 | 0x45 | … | 0xFF | 0xFE | 0x00 | 0x68 | 0x67 | 0x65
TAG | Set | valid | Data
0x000 | 0 | 0 | (64B of data)
0xFFF | 0 | 1 | (64B of data)
0xFFF | 1 | 1 | (64B of data)
0x123 | 1 | 1 | (64B of data)
0x456 | 42 | 1 | (64B of data)
0xFFF | 42 | 1 | (64B of data)
Hit!

## Slide 46: Summary
The notion of storing data is a complicated one.
  Different technologies have different strengths (and costs)
  Often trade-off between:
    fast / small, expensive
    slow / big, cheap
  Hardware designs attempt to accommodate a variety of technologies.
    Often using fast/small memories to act as a “cache” for slower ones.
Caches can be arranged in several ways:
  Blocks go anywhere (fully-associative)
  Blocks go in particular slots (direct-mapped / 1-way associative)
  Hybrid: Blocks go to particular slots… but then can go in any bin in that slot.
Caches attempt to exploit temporal and spatial locality of programs.
  And even a slight improvement to hit rate can dramatically improve overall performance of a program!