## Slide 1: Network Programming

## Slide 2: A Client-Server Transaction
Most network applications are based on the client-server model:
  A server process and one or more client processes
  Server manages some resource
  Server provides service by manipulating resource for clients
  Server activated by request from client (vending machine analogy)
Client
process
Server
process
1. Client sends request
3. Server sends response
4. Client
handles
response
2. Server
handles
request
Resource
Note: clients and servers are processes running on hosts
(can be the same or different hosts)
2

## Slide 3: Hardware Organization of a Network Host
main
memory
I/O
bridge
MI
ALU
register file
CPU chip
system bus
memory bus
disk
controller
graphics
adapter
USB
controller
mouse
keyboard
monitor
disk
I/O bus
Expansion slots
network
adapter
network
3

## Slide 4: Computer Networks
A network is a hierarchical system of boxes and wires organized by geographical proximity
  SAN* (System Area Network) spans cluster or machine room
    Switched Ethernet, Quadrics QSW, …
  LAN (Local Area Network) spans a building or campus
    Ethernet is most prominent example
  WAN (Wide Area Network) spans country or world
    Typically high-speed point-to-point phone lines
An internetwork (internet) is an interconnected set of networks
  The Global IP Internet (uppercase “I”) is the most famous example of an internet (lowercase “i”)
* Not to be confused with a Storage Area Network
4

## Slide 5: Logical Structure of an internet
Ad hoc interconnection of networks
  No particular topology
  Vastly different router & link capacities
Send packets from source to destination by hopping through networks
  Router forms bridge from one network to another
  Different packets may take different routes
router
router
router
router
router
router
host
host
5

## Slide 6: The Notion of an internet Protocol
How is it possible to send bits across incompatible LANs and WANs?
Solution: protocol software running on each host and router
  Protocol is a set of rules that governs how hosts and routers should cooperate when they transfer data from network to network.
  Smooths out the differences between the different networks
6

## Slide 7: What Does an internet Protocol Do?
Provides a naming scheme
  An internet protocol defines a uniform format for host addresses
  Each host (and router) is assigned at least one of these internet addresses that uniquely identifies it
Provides a delivery mechanism
  An internet protocol defines a standard transfer unit (packet)
  Packet consists of header and payload
    Header: contains info such as packet size, source and destination addresses
    Payload: contains data bits sent from source host
7

## Slide 8: Global IP Internet (upper case)
Most famous example of an internet
Based on the TCP/IP protocol family
  IP (Internet Protocol)
    Provides basic naming scheme and unreliable delivery capability of packets (datagrams) from host-to-host
  UDP (Unreliable Datagram Protocol)
    Uses IP to provide unreliable datagram delivery from process-to-process
  TCP (Transmission Control Protocol)
    Uses IP to provide reliable byte streams from process-to-process over connections
Accessed via a mix of Unix file I/O and functions from the sockets interface
8

## Slide 9: Hardware and Software Organization of an Internet Application
TCP/IP
Client
Network
adapter
Global IP Internet
TCP/IP
Server
Network
adapter
Internet client host
Internet server host
Sockets interface
(system calls)
Hardware interface
(interrupts)
User code
Kernel code
Hardware
and firmware
9

## Slide 10: A Programmer’s View of the Internet
1. Hosts are mapped to a set of 32-bit IP addresses
  128.2.203.179
2. The set of IP addresses is mapped to a set of identifiers called Internet domain names
  136.142.156.73 is mapped to www.cs.pitt.edu
3. A process on one Internet host can communicate with a process on another Internet host over a connection
10

## Slide 11: (1) IP Addresses
32-bit IP addresses are stored in an IP address struct
  IP addresses are always stored in memory in network byte order (big-endian byte order)
  True in general for any integer transferred in a packet header from one machine to another.
    E.g., the port number used to identify an Internet connection.
/* Internet address structure */
struct in_addr {
uint32_t s_addr; /* network byte order (big-endian) */
};

## Slide 12: Dotted Decimal Notation
By convention, each byte in a 32-bit IP address is represented by its decimal value and separated by a period
    IP address: 0x8002C2F2 = 128.2.194.242
Use getaddrinfo and getnameinfo functions to convert between IP addresses and dotted decimal format.

## Slide 13: (2) Internet Domain Names
.net
.edu
.gov
.com
pitt
berkeley
mit
cs
sci
thoth
136.142.23.51
unnamed root
www
136.142.156.73
amazon
www
54.230.48.28
First-level domain names
Second-level domain names
Third-level domain names

## Slide 14: Domain Naming System (DNS)
The Internet maintains a mapping between IP addresses and domain names in a huge worldwide distributed database called DNS
Conceptually, programmers can view the DNS database as a collection of millions of host entries.
  Each host entry defines the mapping between a set of domain names and IP addresses.

## Slide 15: Properties of DNS Mappings
Can explore properties of DNS mappings using nslookup
  (Output edited for brevity)
Each host has a locally defined domain name localhost which always maps to the loopback address 127.0.0.1
Use hostname to determine real domain name of local host:
linux> nslookup localhost
Address: 127.0.0.1
linux> hostname
thoth.cs.pitt.edu

## Slide 16: Properties of DNS Mappings (cont)
Simple case: one-to-one mapping between domain name and IP address:
Multiple domain names mapped to the same IP address:
linux> nslookup thoth.cs.cmu.edu
Address: 136.142.23.51
linux> nslookup cs.pitt.edu
Address: 136.142.156.73
linux> nslookup sci.pitt.edu
Address: 136.142.156.73

## Slide 17: Properties of DNS Mappings (cont)
Multiple domain names mapped to multiple IP addresses:
Some valid domain names don’t map to any IP address:
linux> nslookup www.twitter.com
Address: 104.244.42.65
Address: 104.244.42.129
Address: 104.244.42.193
Address: 104.244.42.1
linux> nslookup www.twitter.com
Address: 104.244.42.129
Address: 104.244.42.65
Address: 104.244.42.193
Address: 104.244.42.1
linux> nslookup bla.cs.pitt.edu
(No Address given)

## Slide 18: (3) Internet Connections
Clients and servers communicate by sending streams of bytes over connections. Each connection is:
  Point-to-point: connects a pair of processes.
  Full-duplex: data can flow in both directions at the same time,
  Reliable: stream of bytes sent by the source is eventually received by the destination in the same order it was sent.
A socket is an endpoint of a connection
  Socket address is an IPaddress:port pair
A port is a 16-bit integer that identifies a process:
  Ephemeral port: Assigned automatically by client kernel when client makes a connection request.
  Well-known port: Associated with some service provided by a server (e.g., port 80 is associated with Web servers)

## Slide 19: Well-known Service Names and Ports
Popular services have permanently assigned well-known ports and corresponding well-known service names:
  echo servers: echo 7
  ftp servers: ftp 21
  ssh servers: ssh 22
  email servers: smtp 25
  Web servers: http 80
Mappings between well-known ports and service names is contained in the file /etc/services on each Linux machine.

## Slide 20: Anatomy of a Connection
A connection is uniquely identified by the socket addresses of its endpoints (socket pair)
  (cliaddr:cliport, servaddr:servport)
Connection socket pair
(128.2.194.242:51213, 208.216.181.15:80)
Server
(port 80)
Client
Client socket address
128.2.194.242:51213
Server socket address
208.216.181.15:80
Client host address
128.2.194.242
Server host address
208.216.181.15
51213 is an ephemeral port
allocated by the kernel
80 is a well-known port
associated with Web servers

## Slide 21: Using Ports to Identify Services
Web server
(port 80)
Client host
Server host 128.2.194.242
Echo server
(port 7)
Service request for
128.2.194.242:80
(i.e., the Web server)
Web server
(port 80)
Echo server
(port 7)
Service request for
128.2.194.242:7
(i.e., the echo server)
Kernel
Kernel
Client
Client

## Slide 22: Sockets Interface
Set of system-level functions used in conjunction with Unix I/O to build network applications.
Created in the early 80’s as part of the original Berkeley distribution of Unix that contained an early version of the Internet protocols.
Available on all modern systems
  Unix variants, Windows, OS X, IOS, Android, ARM

## Slide 23: Sockets
Client
Server
What is a socket?
  To the kernel, a socket is an endpoint of communication
  To an application, a socket is a file descriptor that lets the application read/write from/to the network
    Remember: All Unix I/O devices, including networks, are modeled as files
Clients and servers communicate with each other by reading from and writing to socket descriptors
The main distinction between regular file I/O and socket I/O is how the application “opens” the socket descriptors
clientfd
serverfd

## Slide 24: Socket Programming Example
Echo server and client
Server
  Accepts connection request
  Repeats back lines as they are typed
Client
  Requests connection to server
  Repeatedly:
    Read line from terminal
    Send to server
    Read reply from server
    Print line to terminal

## Slide 25: Echo Server/Client Session Example
thoth $ ./echoserver
Server connected to client. (A)
server received 26 bytes (B)
server received 17 bytes (C)
thoth $ ./echoclient (A)
This line is being echoed (B)
This line is being echoed
This one is, too (C)
This one is, too
^D
Client
Server

## Slide 26
5. Drop client
4. Disconnect client
3. Exchange
data
2. Start client
1. Start server
Client / Server
Session
Client
Server
socket read
socket write
socket read
terminal write
terminal read
socket write
Connection
request
socket read
close
close
EOF
accept
listen
connect
Await connection
request from client
Echo Server + Client Structure

## Slide 27
5. Drop client
4. Disconnect client
3. Exchange
data
2. Start client
1. Start server
Client / Server
Session
Client
Server
read
write
read
fputs
fgets
write
Connection
request
read
close
close
EOF
Await connection
request from client
accept
listen
connect
Echo Server + Client Structure

## Slide 28: Echo Server: Main Routine
#include <stdio.h> // fgets, etc
#include <sys/socket.h> // socket API
#include <arpa/inet.h> // inet functions, htons
#include <unistd.h> // read/close system calls
#include <stdlib.h> // exit
#include <string.h> // strlen
#define PORT 9997
int main(void) {
// Creating socket file descriptor (using internet protocol)
int server_fd = socket(AF_INET, SOCK_STREAM, 0);
if (server_fd == 0) {
perror("socket failed");
exit(EXIT_FAILURE);
}
// We want to use the internet protocol
struct sockaddr_in address;
address.sin_family = AF_INET;
address.sin_addr.s_addr = INADDR_ANY;
address.sin_port = htons(PORT);
// Bind socket to the port (so it listens to that port)
int result = bind(server_fd, (struct sockaddr *)&address, sizeof(address));
if (result < 0) {
perror("bind failed");
exit(EXIT_FAILURE);
}
C (gcc -o echoserver echoserver.c)
We create a socket.
// Listen for connections
result = listen(server_fd, 3);
if (result < 0) {
perror("listen");
exit(EXIT_FAILURE);
}
// Listen will return when a connection is requested...
// Accept that connection
int addrlen = sizeof(address);
int new_socket = accept(server_fd, (struct sockaddr *)&address,
(socklen_t*)&addrlen);
if (new_socket < 0) {
perror("accept");
exit(EXIT_FAILURE);
}
printf("Server connected to client.\n");
char buffer[1024] = {0};
int count = 0;
do {
// Read data (it waits until data is available)
count = read(new_socket, buffer, 1024);
printf("Server received %d bytes.\n", count);
buffer[count] = '\0';
write(new_socket, buffer, strlen(buffer));
} while(count);
close(new_socket);
close(server_fd);
return 0;
}
We define what port and
protocol we want
We bind ourselves to that port.
We wait until somebody requests a connection.
We accept that connection.
We wait until data arrives and read it.
We write it back out. Stopping our
loop when nothing was read.
We close all of our connections.

## Slide 29
2. Start client
Client
3. Exchange
data
1. Start server
Client / Server
Session
Server
read
write
read
fputs
fgets
write
Connection
request
read
close
close
EOF
Await connection
request from client
accept
listen
connect
Echo Server + Client Structure

## Slide 30: Echo Client: Main Routine
#include <stdio.h> // fgets, etc
#include <sys/socket.h> // socket API
#include <arpa/inet.h> // inet functions, htons
#include <unistd.h> // read/close system calls
#include <string.h> // strlen
#define PORT 9997
int main(void) {
// Creating socket file descriptor (using internet protocol)
int sock = socket(AF_INET, SOCK_STREAM, 0);
if (sock < 0) {
printf("\n Socket creation error \n");
return -1;
}
struct sockaddr_in serv_addr;
serv_addr.sin_family = AF_INET;
serv_addr.sin_port = htons(PORT);
// Convert IPv4 and IPv6 addresses from text to binary form
if (inet_pton(AF_INET, "127.0.0.1", &serv_addr.sin_addr)<=0) {
printf("\nInvalid address / Address not supported \n");
return -1;
}
C (gcc -o echoclient echoclient.c)
int result = connect(sock,
(struct sockaddr *)&serv_addr,
sizeof(serv_addr));
if (result < 0) {
printf("\nConnection Failed \n");
return -1;
}
char buffer[1024] = {0};
int count = 0;
do {
if (fgets(buffer, 1024, stdin) == NULL) {
break; // Exit when line is empty (CTRL+D is pressed)
}
write(sock, buffer, strlen(buffer));
count = read(sock, buffer, 1023);
buffer[count] = '\0';
fputs(buffer, stdout);
} while(count);
close(sock);
return 0;
}
We create a socket.
Using the Internet protocol.
Connecting to localhost
Actually request a connection.
If we got here, the server accepted our connection!
This loop reads from stdin (user input)
We write everything to the server!
And print out everything the server sends us.
We clean up when the loop ends (when no user input via CTRL+D)

## Slide 31: Read and write system calls
Same interface used to read/write files.
  Because sockets are also files! Neat.
  read returns a count of 0 only if it encounters EOF
    So, it is useful to notice if the other machine disconnected.
  Calls to read and write can be interleaved arbitrarily on the same file descriptor (socket, file on disk, etc)
#include <unistd.h>
ssize_t read(int fd, void *usrbuf, size_t n);
ssize_t write(int fd, void *usrbuf, size_t n);
Return: number of bytes transferred if OK, 0 on EOF (read only), -1 on error

## Slide 32: Sockets Interface
Client / Server
Session
Client
Server
socket
socket
bind
listen
read
write
read
write
Connection
request
read
close
close
EOF
Await connection
request from
next client
listen
connect
accept
connect
getaddrinfo
getaddrinfo

## Slide 33: connect/accept Illustrated
listenfd(3)
Client
1. Server blocks in accept, waiting for connection request on listening descriptor listenfd
clientfd
Server
listenfd(3)
Client
clientfd
Server
2. Client makes connection request by calling and blocking in connect
Connection
request
listenfd(3)
Client
clientfd
Server
3. Server returns connfd from accept. Client returns from connect. Connection is now established between clientfd and connfd
connfd(4)

## Slide 34: Connected vs. Listening Descriptors
Listening descriptor
  End point for client connection requests
  Created once and exists for lifetime of the server
Connected descriptor
  End point of the connection between client and server
  A new descriptor is created each time the server accepts a connection request from a client
  Exists only as long as it takes to service client
Why the distinction?
  Allows for concurrent servers that can communicate over many client connections simultaneously
    E.g., Each time we receive a new request, we fork a child to handle the request

## Slide 35: Testing Servers Using telnet
The telnet program is invaluable for testing servers that transmit ASCII strings over Internet connections
  Our simple echo server
  Web servers
  Mail servers
Usage:
  linux> telnet <host> <portnumber>
  Creates a connection with a server running on <host> and listening on port <portnumber>

## Slide 36: Testing the Echo Server With telnet
occam.dev $ ./echoserver 10001
Server connected to client.
Server received 11 bytes
Server received 8 bytes
thoth $ telnet occam.dev 10001
Trying 142.4.212.185...
Connected to occam.dev (142.4.212.185).
Escape character is '^]'.
Hi there!
Hi there!
Howdy!
Howdy!
^]  This means CTRL+]
telnet> quit
Connection closed.
thoth $

## Slide 37: Web Server Basics
Clients and servers communicate using the HyperText Transfer Protocol (HTTP)
  Client and server establish TCP connection
  Client requests content
  Server responds with requested content
  Client and server close connection (eventually)
Current version is HTTP/1.1
  RFC 2616, June, 1999.
Web
server
HTTP request
HTTP response
(content)
Web
client
(browser)
http://www.w3.org/Protocols/rfc2616/rfc2616.html
IP
TCP
HTTP
Datagrams
Streams
Web content

## Slide 38: Web Content
Web servers return content to clients
  content: a sequence of bytes with an associated MIME (Multipurpose Internet Mail Extensions) type
Example MIME types
  text/html HTML document
  text/plain Unformatted text
  image/gif Binary image encoded in GIF format
  image/png Binar image encoded in PNG format
  image/jpeg Binary image encoded in JPEG format
You can find the complete list of MIME types at:
http://www.iana.org/assignments/media-types/media-types.xhtml

## Slide 39: Static and Dynamic Content
The content returned in HTTP responses can be either static or dynamic
  Static content: content stored in files and retrieved in response to an HTTP request
    Examples: HTML files, images, audio clips, Javascript programs
    Request identifies which content file
  Dynamic content: content produced on-the-fly in response to an HTTP request
    Example: content produced by a program executed by the server on behalf of the client
    Request identifies file containing executable code
Bottom line: Web content is associated with a file that is managed by the server

## Slide 40: URLs and how clients and servers use them
Unique name for a file: URL (Universal Resource Locator)
Example URL: http://www.google.edu:80/index.html
Clients use prefix (http://www.google.edu:80) to infer:
  What kind (protocol) of server to contact (HTTP)
  Where the server is (www.google.com)
  What port it is listening on (80)
Servers use suffix (/index.html) to:
  Determine if request is for static or dynamic content.
    No hard and fast rules for this
    One convention: executables reside in cgi-bin directory
  Find file on file system
    Initial “/” in suffix denotes home directory for requested content.
    Minimal suffix is “/”, which server expands to configured default filename (usually, index.html)

## Slide 41: HTTP Requests
HTTP request is a request line, followed by zero or more request headers
Request line: <method> <uri> <version>
  <method> is one of GET, POST, OPTIONS, HEAD, PUT, DELETE, or TRACE
  <uri> is typically URL for proxies, URL suffix for servers
    A URL is a type of URI (Uniform Resource Identifier)
    See http://www.ietf.org/rfc/rfc2396.txt
  <version> is HTTP version of request (HTTP/1.0 or HTTP/1.1)
Request headers: <header name>: <header data>
  Provide additional information to the server

## Slide 42: HTTP Responses
HTTP response is a response line followed by zero or more response headers, possibly followed by content, with blank line (“\r\n”) separating headers from content.
Response line:
<version> <status code> <status msg>
  <version> is HTTP version of the response
  <status code> is numeric status
  <status msg> is corresponding English text
    200 OK Request was handled without error
    301 Moved Provide alternate URL
    404 Not found Server couldn’t find the file
Response headers: <header name>: <header data>
  Provide additional information about response
  Content-Type: MIME type of content in response body
  Content-Length: Length of content in response body

## Slide 43: Example HTTP Transaction
whaleshark> telnet www.cmu.edu 80 Client: open connection to server
Trying 128.2.42.52... Telnet prints 3 lines to terminal
Connected to WWW-CMU-PROD-VIP.ANDREW.cmu.edu.
Escape character is '^]'.
GET / HTTP/1.1 Client: request line
Host: www.cmu.edu Client: required HTTP/1.1 header
Client: empty line terminates headers
HTTP/1.1 301 Moved Permanently Server: response line
Date: Wed, 05 Nov 2014 17:05:11 GMT Server: followed by 5 response headers
Server: Apache/1.3.42 (Unix) Server: this is an Apache server
Location: http://www.cmu.edu/index.shtml Server: page has moved here
Transfer-Encoding: chunked Server: response body will be chunked
Content-Type: text/html; charset=... Server: expect HTML in response body
Server: empty line terminates headers
15c Server: first line in response body
<HTML><HEAD> Server: start of HTML content
…
</BODY></HTML> Server: end of HTML content
0 Server: last line in response body
Connection closed by foreign host. Server: closes connection
HTTP standard requires that each text line end with “\r\n”
Blank line (“\r\n”) terminates request and response headers
Notes: Resume here on Tuesday

## Slide 44: Example HTTP Transaction, Take 2
whaleshark> telnet www.cmu.edu 80 Client: open connection to server
Trying 128.2.42.52... Telnet prints 3 lines to terminal
Connected to WWW-CMU-PROD-VIP.ANDREW.cmu.edu.
Escape character is '^]'.
GET /index.shtml HTTP/1.1 Client: request line
Host: www.cmu.edu Client: required HTTP/1.1 header
Client: empty line terminates headers
HTTP/1.1 200 OK Server: response line
Date: Wed, 05 Nov 2014 17:37:26 GMT Server: followed by 4 response headers
Server: Apache/1.3.42 (Unix)
Transfer-Encoding: chunked
Content-Type: text/html; charset=...
Server: empty line terminates headers
1000 Server: begin response body
<html ..> Server: first line of HTML content
…
</html>
0 Server: end response body
Connection closed by foreign host. Server: close connection

## Slide 45: Proxies
A proxy is an intermediary between a client and an origin server
  To the client, the proxy acts like a server
  To the server, the proxy acts like a client
  This is what you will be implementing in Proxy Lab
Client
Proxy
Origin
Server
1. Client request
2. Proxy request
3. Server response
4. Proxy response

## Slide 46: Why Proxies?
Can perform useful functions as requests and responses pass by
  Examples: Caching, logging, anonymization, filtering, transcoding
Client
A
Proxy
cache
Origin
Server
Request foo.html
Request foo.html
foo.html
foo.html
Client
B
Request foo.html
foo.html
Fast inexpensive local network
Slower more expensive global network

## Slide 47: Sockets Interface
Client / Server
Session
Client
Server
socket
socket
bind
listen
rio_readlineb
rio_writen
rio_readlineb
rio_writen
Connection
request
rio_readlineb
close
close
EOF
Await connection
request from
next client
open_listenfd
open_clientfd
accept
connect
getaddrinfo
getaddrinfo
SA list
SA list

## Slide 48: Sockets Interface: socket
Clients and servers use the socket function to create a socket descriptor:
Example:
Protocol specific! Best practice is to use getaddrinfo to generate the parameters automatically, so that code is protocol independent.
int socket(int domain, int type, int protocol)
int clientfd = socket(AF_INET, SOCK_STREAM, 0);
Indicates that we are using 32-bit IPV4 addresses
Indicates that the socket will be the end point of a connection

## Slide 49: Sockets Interface
Client / Server
Session
Client
Server
socket
socket
bind
listen
read
write
read
write
Connection
request
read
close
close
EOF
Await connection
request from
next client
open_listenfd
open_clientfd
accept
connect
getaddrinfo
getaddrinfo
listenfd
clientfd
SA list
SA list

## Slide 50: Sockets Interface: bind
A server uses bind to ask the kernel to associate the server’s socket address with a socket descriptor:
Recall: typedef struct sockaddr SA;
Process can read bytes that arrive on the connection whose endpoint is addr by reading from descriptor sockfd
Similarly, writes to sockfd are transferred along connection whose endpoint is addr
Best practice is to use getaddrinfo to supply the arguments addr and addrlen.
int bind(int sockfd, SA *addr, socklen_t addrlen);

## Slide 51: Sockets Interface
Client / Server
Session
Client
Server
socket
socket
bind
listen
read
write
read
write
Connection
request
read
close
close
EOF
Await connection
request from
next client
open_listenfd
open_clientfd
accept
connect
getaddrinfo
getaddrinfo
SA list
listenfd
listenfd <-> SA
SA list
clientfd

## Slide 52: Sockets Interface: listen
By default, kernel assumes that descriptor from socket function is an active socket that will be on the client end of a connection.
A server calls the listen function to tell the kernel that a descriptor will be used by a server rather than a client:
Converts sockfd from an active socket to a listening socket that can accept connection requests from clients.
backlog is a hint about the number of outstanding connection requests that the kernel should queue up before starting to refuse requests.
int listen(int sockfd, int backlog);

## Slide 53: Sockets Interface
Client / Server
Session
Client
Server
socket
socket
bind
listen
read
write
read
write
Connection
request
rio_readlineb
close
close
EOF
Await connection
request from
next client
open_listenfd
open_clientfd
accept
connect
getaddrinfo
getaddrinfo
SA list
clientfd
SA list
listenfd
listenfd <-> SA
listening listenfd

## Slide 54: Sockets Interface: accept
Servers wait for connection requests from clients by calling accept:
Waits for connection request to arrive on the connection bound to listenfd, then fills in client’s socket address in addr and size of the socket address in addrlen.
Returns a connected descriptor that can be used to communicate with the client via Unix I/O routines.
int accept(int listenfd, SA *addr, int *addrlen);

## Slide 55: Sockets Interface
Client / Server
Session
Client
Server
socket
socket
bind
listen
read
write
read
write
Connection
request
read
close
close
EOF
Await connection
request from
next client
open_listenfd
open_clientfd
accept
connect
getaddrinfo
getaddrinfo
listening listenfd
SA list
SA list
clientfd
listenfd
listenfd <-> SA

## Slide 56: Sockets Interface: connect
A client establishes a connection with a server by calling connect:
Attempts to establish a connection with server at socket address addr
  If successful, then clientfd is now ready for reading and writing.
  Resulting connection is characterized by socket pair
  (x:y, addr.sin_addr:addr.sin_port)
    x is client address
    y is ephemeral port that uniquely identifies client process on client host
Best practice is to use getaddrinfo to supply the arguments addr and addrlen.
int connect(int clientfd, SA *addr, socklen_t addrlen);

## Slide 57: Sockets Interface
Client / Server
Session
Client
Server
socket
socket
bind
listen
read
write
read
write
Connection
request
rio_readlineb
close
close
EOF
Await connection
request from
next client
open_listenfd
open_clientfd
accept
connect
getaddrinfo
getaddrinfo
listening listenfd
connected connfd
connected (to SA) clientfd
SA list
SA list
clientfd
listenfd
listenfd <-> SA

## Slide 58: Sockets Interface
Client / Server
Session
Client
Server
socket
socket
bind
listen
read
write
read
write
Connection
request
read
close
close
EOF
Await connection
request from
next client
open_listenfd
open_clientfd
accept
connect
getaddrinfo
getaddrinfo

## Slide 59: Sockets Helper: open_clientfd
Establish a connection with a server
int open_clientfd(char *hostname, char *port) {
int clientfd;
struct addrinfo hints, *listp, *p;
/* Get a list of potential server addresses */
memset(&hints, 0, sizeof(struct addrinfo));
hints.ai_socktype = SOCK_STREAM; /* Open a connection */
hints.ai_flags = AI_NUMERICSERV; /* …using numeric port arg. */
hints.ai_flags |= AI_ADDRCONFIG; /* Recommended for connections */
getaddrinfo(hostname, port, &hints, &listp);
csapp.c

## Slide 60: getaddrinfo Linked List
Clients: walk this list, trying each socket address in turn, until the calls to socket and connect succeed.
Servers: walk the list until calls to socket and bind succeed.
ai_canonname
result
ai_addr
ai_next
addrinfo structs
Socket address structs
NULL
ai_addr
ai_next
NULL
ai_addr
NULL

## Slide 61: Sockets Helper: open_clientfd (cont)
/* Walk the list for one that we can successfully connect to */
for (p = listp; p; p = p->ai_next) {
/* Create a socket descriptor */
if ((clientfd = socket(p->ai_family, p->ai_socktype,
p->ai_protocol)) < 0)
continue; /* Socket failed, try the next */
/* Connect to the server */
if (connect(clientfd, p->ai_addr, p->ai_addrlen) != -1)
break; /* Success */
close(clientfd); /* Connect failed, try another */
}
/* Clean up */
freeaddrinfo(listp);
if (!p) /* All connects failed */
return -1;
else /* The last connect succeeded */
return clientfd;
}
csapp.c

## Slide 62: Sockets Interface
Client / Server
Session
Client
Server
socket
socket
bind
listen
read
write
read
write
Connection
request
read
close
close
EOF
Await connection
request from
next client
open_listenfd
open_clientfd
accept
connect
getaddrinfo
getaddrinfo

## Slide 63: Sockets Helper: open_listenfd
Create a listening descriptor that can be used to accept connection requests from clients.
int open_listenfd(char *port)
{
struct addrinfo hints, *listp, *p;
int listenfd, optval=1;
/* Get a list of potential server addresses */
memset(&hints, 0, sizeof(struct addrinfo));
hints.ai_socktype = SOCK_STREAM; /* Accept connect. */
hints.ai_flags = AI_PASSIVE | AI_ADDRCONFIG; /* …on any IP addr */
hints.ai_flags |= AI_NUMERICSERV; /* …using port no. */
getaddrinfo(NULL, port, &hints, &listp);
csapp.c

## Slide 64: Sockets Helper: open_listenfd (cont)
/* Walk the list for one that we can bind to */
for (p = listp; p; p = p->ai_next) {
/* Create a socket descriptor */
if ((listenfd = socket(p->ai_family, p->ai_socktype,
p->ai_protocol)) < 0)
continue; /* Socket failed, try the next */
/* Eliminates "Address already in use" error from bind */
setsockopt(listenfd, SOL_SOCKET, SO_REUSEADDR,
(const void *)&optval , sizeof(int));
/* Bind the descriptor to the address */
if (bind(listenfd, p->ai_addr, p->ai_addrlen) == 0)
break; /* Success */
close(listenfd); /* Bind failed, try the next */
}
csapp.c

## Slide 65: Sockets Helper: open_listenfd (cont)
/* Clean up */
freeaddrinfo(listp);
if (!p) /* No address worked */
return -1;
/* Make it a listening socket ready to accept conn. requests */
if (listen(listenfd, LISTENQ) < 0) {
close(listenfd);
return -1;
}
return listenfd;
}
csapp.c
Key point: open_clientfd and open_listenfd are both independent of any particular version of IP.

## Slide 66
Case Study
Tiny Web Server

## Slide 67: Tiny Web Server
Tiny Web server described in textbook (CS:APP)
  Tiny is a sequential Web server
  Serves static and dynamic content to real browsers
    text files, HTML files, GIF, PNG, and JPEG images
  239 lines of commented C code
  Not as complete or robust as a real Web server
    You can break it with poorly-formed HTTP requests (e.g., terminate lines with “\n” instead of “\r\n”)

## Slide 68: Tiny Operation
Accept connection from client
Read request from client (via connected socket)
Split into <method> <uri> <version>
  If method not GET, then return error
If URI contains “cgi-bin” then serve dynamic content
  (Would do wrong thing if had file “abcgi-bingo.html”)
  Fork process to execute program
Otherwise serve static content
  Copy file to output

## Slide 69: Tiny Serving Static Content
void serve_static(int fd, char *filename, int filesize)
{
int srcfd;
char *srcp, filetype[MAXLINE], buf[MAXBUF];
/* Send response headers to client */
get_filetype(filename, filetype);
sprintf(buf, "HTTP/1.0 200 OK\r\n");
sprintf(buf, "%sServer: Tiny Web Server\r\n", buf);
sprintf(buf, "%sConnection: close\r\n", buf);
sprintf(buf, "%sContent-length: %d\r\n", buf, filesize);
sprintf(buf, "%sContent-type: %s\r\n\r\n", buf, filetype);
write(fd, buf, strlen(buf));
/* Send response body to client */
srcfd = open(filename, O_RDONLY, 0);
srcp = mmap(0, filesize, PROT_READ, MAP_PRIVATE, srcfd, 0);
close(srcfd);
write(fd, srcp, filesize);
munmap(srcp, filesize);
}
tiny.c

## Slide 70: Serving Dynamic Content
Client sends request to server
If request URI contains the string “/cgi-bin”, the Tiny server assumes that the request is for dynamic content
Client
Server
GET /cgi-bin/env.pl HTTP/1.1

## Slide 71: Serving Dynamic Content (cont)
The server creates a child process and runs the program identified by the URI in that process
Client
Server
env.pl
fork/exec

## Slide 72: Serving Dynamic Content (cont)
The child runs and generates the dynamic content
The server captures the content of the child and forwards it without modification to the client
Client
Server
env.pl
Content
Content

## Slide 73: Issues in Serving Dynamic Content
How does the client pass program arguments to the server?
How does the server pass these arguments to the child?
How does the server pass other info relevant to the request to the child?
How does the server capture the content produced by the child?
These issues are addressed by the Common Gateway Interface (CGI) specification.
Client
Server
Content
Content
Request
Create
env.pl

## Slide 74: CGI
Because the children are written according to the CGI spec, they are often called CGI programs.
However, CGI really defines a simple standard for transferring information between the client (browser), the server, and the child process.
CGI is the original standard for generating dynamic content. Has been largely replaced by other, faster techniques:
  E.g., fastCGI, Apache modules, Java servlets, Rails controllers
  Avoid having to create process on the fly (expensive and slow).

## Slide 75: The add.com Experience
Output page
host
port
CGI program
arguments

## Slide 76: Serving Dynamic Content With GET
Question: How does the client pass arguments to the server?
Answer: The arguments are appended to the URI
Can be encoded directly in a URL typed to a browser or a URL in an HTML link
  http://add.com/cgi-bin/adder?15213&18213
  adder is the CGI program on the server that will do the addition.
  argument list starts with “?”
  arguments separated by “&”
  spaces represented by “+” or “%20”

## Slide 77: Serving Dynamic Content With GET
URL suffix:
  cgi-bin/adder?15213&18213
Result displayed on browser:
Welcome to add.com: THE Internet addition portal.
The answer is: 15213 + 18213 = 33426
Thanks for visiting!

## Slide 78: Serving Dynamic Content With GET
Question: How does the server pass these arguments to the child?
Answer: In environment variable QUERY_STRING
  A single string containing everything after the “?”
  For add: QUERY_STRING = “15213&18213”
/* Extract the two arguments */
if ((buf = getenv("QUERY_STRING")) != NULL) {
p = strchr(buf, '&');
*p = '\0';
strcpy(arg1, buf);
strcpy(arg2, p+1);
n1 = atoi(arg1);
n2 = atoi(arg2);
}
adder.c

## Slide 79: Serving Dynamic Content with GET
void serve_dynamic(int fd, char *filename, char *cgiargs)
{
char buf[MAXLINE], *emptylist[] = { NULL };
/* Return first part of HTTP response */
sprintf(buf, "HTTP/1.0 200 OK\r\n");
Rio_writen(fd, buf, strlen(buf));
sprintf(buf, "Server: Tiny Web Server\r\n");
Rio_writen(fd, buf, strlen(buf));
if (Fork() == 0) { /* Child */
/* Real server would set all CGI vars here */
setenv("QUERY_STRING", cgiargs, 1);
Dup2(fd, STDOUT_FILENO); /* Redirect stdout to client */
Execve(filename, emptylist, environ); /* Run CGI program */
}
Wait(NULL); /* Parent waits for and reaps child */
}
Question: How does the server capture the content produced by the child?
Answer: The child generates its output on stdout. Server uses dup2 to redirect stdout to its connected socket.
tiny.c

## Slide 80: Serving Dynamic Content with GET
/* Make the response body */
sprintf(content, "Welcome to add.com: ");
sprintf(content, "%sTHE Internet addition portal.\r\n<p>", content);
sprintf(content, "%sThe answer is: %d + %d = %d\r\n<p>",
content, n1, n2, n1 + n2);
sprintf(content, "%sThanks for visiting!\r\n", content);
/* Generate the HTTP response */
printf("Content-length: %d\r\n", (int)strlen(content));
printf("Content-type: text/html\r\n\r\n");
printf("%s", content);
fflush(stdout);
exit(0);
adder.c
Notice that only the CGI child process knows the content type and length, so it must generate those headers.

## Slide 81: Serving Dynamic Content With GET
bash:makoshark> telnet whaleshark.ics.cs.cmu.edu 15213
Trying 128.2.210.175...
Connected to whaleshark.ics.cs.cmu.edu (128.2.210.175).
Escape character is '^]'.
GET /cgi-bin/adder?15213&18213 HTTP/1.0
HTTP/1.0 200 OK
Server: Tiny Web Server
Connection: close
Content-length: 117
Content-type: text/html
Welcome to add.com: THE Internet addition portal.
<p>The answer is: 15213 + 18213 = 33426
<p>Thanks for visiting!
Connection closed by foreign host.
bash:makoshark>
HTTP request sent by client
HTTP response generated
by the server
HTTP response generated
by the CGI program

## Slide 82: For More Information
W. Richard Stevens et. al. “Unix Network Programming: The Sockets Networking API”, Volume 1, Third Edition, Prentice Hall, 2003
  THE network programming bible.
Michael Kerrisk, “The Linux Programming Interface”, No Starch Press, 2010
  THE Linux programming bible.
Code examples
  csapp.{.c,h}, hostinfo.c, echoclient.c, echoserveri.c, tiny.c, adder.c
  You can use any of this code in your assignments.

## Slide 83
BONUS SLIDES
The following slides are for those curious.
You will NOT be expected to know this material.

## Slide 84: Lowest Level: Ethernet Segment
Ethernet segment consists of a collection of hosts connected by wires (twisted pairs) to a hub
Spans room or floor in a building
Operation
  Each Ethernet adapter has a unique 48-bit address (MAC address)
    E.g., 00:16:ea:e3:54:e6
  Hosts send bits to any other host in chunks called frames
  Hub slavishly copies each bit from each port to every other port
    Every host sees every bit
  [Note: Hubs are obsolete. Bridges (switches, routers) became cheap enough to replace them]
host
host
host
hub
100 Mb/s
100 Mb/s
port

## Slide 85: Next Level: Bridged Ethernet Segment
Spans building or campus
Bridges cleverly learn which hosts are reachable from which ports and then selectively copy frames from port to port
host
host
host
host
host
hub
hub
bridge
100 Mb/s
100 Mb/s
host
host
hub
100 Mb/s
100 Mb/s
1 Gb/s
host
host
host
bridge
host
host
hub
A
B
C
X
Y

## Slide 86: Conceptual View of LANs
For simplicity, hubs, bridges, and wires are often shown as a collection of hosts attached to a single wire:
host
host
host
...

## Slide 87: Next Level: internets
Multiple incompatible LANs can be physically connected by specialized computers called routers
The connected networks are called an internet (lower case)
host
host
host
...
host
host
host
...
WAN
WAN
LAN 1 and LAN 2 might be completely different, totally incompatible
(e.g., Ethernet, Fibre Channel, 802.11*, T1-links, DSL, …)
router
router
router
LAN 1
LAN 2

## Slide 88: Transferring internet Data Via Encapsulation
LAN2
protocol
software
client
LAN1
adapter
Host A
LAN1
data
(1)
data
PH
FH1
(4)
data
PH
FH2
(6)
data
(8)
data
PH
FH2
(5)
LAN2 frame
protocol
software
LAN1
adapter
LAN2
adapter
Router
data
PH
(3)
FH1
data
PH
FH1
(2)
internet packet
LAN1 frame
(7)
data
PH
FH2
protocol
software
server
LAN2
adapter
Host B
PH: internet packet header
FH: LAN frame header

## Slide 89: Aside: IPv4 and IPv6
The original Internet Protocol, with its 32-bit addresses, is known as Internet Protocol Version 4 (IPv4)
1996: Internet Engineering Task Force (IETF) introduced Internet Protocol Version 6 (IPv6) with 128-bit addresses
  Intended as the successor to IPv4
Majority of Internet traffic still carried by IPv4
We will focus on IPv4, but will show you how to write networking code that is protocol-independent.
IPv6 traffic at Google

## Slide 90: Socket Address Structures
Generic socket address:
  For address arguments to connect, bind, and accept
  Necessary only because C did not have generic (void *) pointers when the sockets interface was designed
  For casting convenience, we adopt the Stevens convention:
  typedef struct sockaddr SA;
struct sockaddr {
uint16_t sa_family; /* Protocol family */
char sa_data[14]; /* Address data */
};
sa_family
Family Specific

## Slide 91: Socket Address Structures
Internet (IPv4) specific socket address:
  Must cast (struct sockaddr_in *) to (struct sockaddr *) for functions that take socket address arguments.
0
0
0
0
0
0
0
0
sa_family
Family Specific
struct sockaddr_in {
uint16_t sin_family; /* Protocol family (always AF_INET) */
uint16_t sin_port; /* Port num in network byte order */
struct in_addr sin_addr; /* IP addr in network byte order */
unsigned char sin_zero[8]; /* Pad to sizeof(struct sockaddr) */
};
sin_port
AF_INET
sin_addr
sin_family

## Slide 92: Host and Service Conversion: getaddrinfo
getaddrinfo is the modern way to convert string representations of hostnames, host addresses, ports, and service names to socket address structures.
  Replaces obsolete gethostbyname and getservbyname funcs.
Advantages:
  Reentrant (can be safely used by threaded programs).
  Allows us to write portable protocol-independent code
    Works with both IPv4 and IPv6
Disadvantages
  Somewhat complex
  Fortunately, a small number of usage patterns suffice in most cases.

## Slide 93: Host and Service Conversion: getaddrinfo
Given host and service, getaddrinfo returns result that points to a linked list of addrinfo structs, each of which points to a corresponding socket address struct, and which contains arguments for the sockets interface functions.
Helper functions:
  freeadderinfo frees the entire linked list.
  gai_strerror converts error code to an error message.
int getaddrinfo(const char *host, /* Hostname or address */
const char *service, /* Port or service name */
const struct addrinfo *hints,/* Input parameters */
struct addrinfo **result); /* Output linked list */
void freeaddrinfo(struct addrinfo *result); /* Free linked list */
const char *gai_strerror(int errcode); /* Return error msg */

## Slide 94: Linked List Returned by getaddrinfo
Clients: walk this list, trying each socket address in turn, until the calls to socket and connect succeed.
Servers: walk the list until calls to socket and bind succeed.
ai_canonname
result
ai_addr
ai_next
addrinfo structs
Socket address structs
NULL
ai_addr
ai_next
NULL
ai_addr
NULL

## Slide 95: addrinfo Struct
Each addrinfo struct returned by getaddrinfo contains arguments that can be passed directly to socket function.
Also points to a socket address struct that can be passed directly to connect and bind functions.
struct addrinfo {
int ai_flags; /* Hints argument flags */
int ai_family; /* First arg to socket function */
int ai_socktype; /* Second arg to socket function */
int ai_protocol; /* Third arg to socket function */
char *ai_canonname; /* Canonical host name */
size_t ai_addrlen; /* Size of ai_addr struct */
struct sockaddr *ai_addr; /* Ptr to socket address structure */
struct addrinfo *ai_next; /* Ptr to next item in linked list */
};

## Slide 96: Host and Service Conversion: getnameinfo
getnameinfo is the inverse of getaddrinfo, converting a socket address to the corresponding host and service.
  Replaces obsolete gethostbyaddr and getservbyport funcs.
  Reentrant and protocol independent.
int getnameinfo(const SA *sa, socklen_t salen, /* In: socket addr */
char *host, size_t hostlen, /* Out: host */
char *serv, size_t servlen, /* Out: service */
int flags); /* optional flags */

## Slide 97: Conversion Example (writing our own nslookup)
int main(int argc, char **argv)
{
struct addrinfo *p, *listp, hints;
char buf[MAXLINE];
int rc, flags;
/* Get a list of addrinfo records */
memset(&hints, 0, sizeof(struct addrinfo));
// hints.ai_family = AF_INET; /* IPv4 only */
hints.ai_socktype = SOCK_STREAM; /* Connections only */
if ((rc = getaddrinfo(argv[1], NULL, &hints, &listp)) != 0) {
fprintf(stderr, "getaddrinfo error: %s\n", gai_strerror(rc));
exit(1);
}
hostinfo.c

## Slide 98: Conversion Example (cont)
/* Walk the list and display each IP address */
flags = NI_NUMERICHOST; /* Display address instead of name */
for (p = listp; p; p = p->ai_next) {
getnameinfo(p->ai_addr, p->ai_addrlen,
buf, MAXLINE, NULL, 0, flags);
printf("%s\n", buf);
}
/* Clean up */
freeaddrinfo(listp);
exit(0);
}
hostinfo.c

## Slide 99: Running hostinfo
whaleshark> ./hostinfo localhost
127.0.0.1
whaleshark> ./hostinfo whaleshark.ics.cs.cmu.edu
128.2.210.175
whaleshark> ./hostinfo twitter.com
199.16.156.230
199.16.156.38
199.16.156.102
199.16.156.198
whaleshark> ./hostinfo google.com
172.217.15.110
2607:f8b0:4004:802::200e